## Slide 1: USB Device Control & Monitoring Framework
Aneesha Jimmis | Cybersecurity Internship Project

## Slide 2: Project Objectives
Detect USB devices in real-time on connect and disconnect events
Extract Vendor ID, Product ID, and Serial Number for device fingerprinting
Verify devices against an allowlist — authorize or flag unknown devices
Monitor file creation, modification, and deletion in USB storage directories
Generate SHA256 hashes for all monitored files to ensure integrity
Produce timestamped audit logs and generate TXT security reports

## Slide 3: Technologies Used
Python 3
  Core language
  Main scripting language for all modules
Pyudev
  USB Monitoring
  Real-time USB event detection via netlink
Watchdog
  File Monitoring
  Filesystem event handler for USB directory
Hashlib
  Integrity
  SHA256 hash generation for file auditing
Logging
  Audit Logging
  Timestamped event logging to usb_audit.log
Kali Linux
  Platform
  Running inside VirtualBox on macOS host

## Slide 4
System Architecture
USB Device Connected
USB Detection
(pyudev)
Device
Fingerprinting
Allowlist
Verification
AUTHORIZED
Allow + Log
UNAUTHORIZED
Block + log
Audit Logging
(usb_audit.log)
File Monitoring
(watchdog)
SHA256 Hashing
(hashlib)
Security Report (report.txt)
Vendor: 05ac = Apple Inc.

## Slide 5
USB Passthrough Configuration (macOS → Kali Linux VM)
Connected iPhone to macOS host machine.
Identified the USB device using:
VBoxManage list usbhost
Retrieved the device UUID, Vendor ID, Product ID, and Serial Number.
Attached the iPhone to the running Kali VM using:
VBoxManage controlvm "Kali" usbattach <UUID>
Approved the VirtualBox permission request on macOS.
Verified successful detection inside Kali Linux.

## Slide 6
System Configuration and Project Files

## Slide 7
System Configuration and Project Files

## Slide 8
System Configuration and Project Files

## Slide 9
System Configuration and Project Files

## Slide 10
Result

## Slide 11
Conclusion
Key Learnings
How pyudev monitors USB hardware events via Linux kernel netlink
Device fingerprinting using Vendor ID / Product ID / Serial Number
Allowlist-based endpoint policy enforcement
File integrity monitoring with SHA256 hashing
Blue team techniques: insider activity tracking